## Slide 1: Novel LArTPC technologies for near detectors
Zoya Vallari
Caltech
October 31, 2024

## Slide 2: The long & Short of oscillation measurements
*Not to scale
neutrino beam
Near Detector
Far Detector
Short baseline O(~100 m)
/
/
neutrino beam
Near Detector
Far Detector
/
Long baseline O(~100 km)
/
Zoya Vallari, NNN 2024

## Slide 3: The long & Short of oscillation measurements
*Not to scale
neutrino beam
Near Detector
Far Detector
Short baseline O(~100 m)
/
/
neutrino beam
Near Detector
Far Detector
/
Long baseline O(~100 km)
/
Sample the beam
before oscillations
Measure oscillations
Zoya Vallari, NNN 2024

## Slide 4: role of near detectors
oscillation probability
detector response
cross-section
neutrino flux
Event rate
FAR DETECTOR
NEAR DETECTOR
Near Detector provides valuable in-situ cancelation and constraints on:
  neutrino flux
  cross-section, and
  detector uncertainties
Zoya Vallari, NNN 2024
*More from Joe Walsh
in tomorrow morning session

## Slide 5: requirements for a near detector?
I. Neutrino Flux
  Measure the flux: not mono-energetic and not well-understood
    Challenge: flux shape differs significantly between the Near and Far detectors due to distance and oscillations
    Solution: Movable NDs*
  Monitor beam stability
Zoya Vallari, NNN 2024
Nature volume 599, pages565–570 (2021)
Flux at ND
Flux at FD
(with assumed value of oscillation parameters)
*More from Akutsu-san in today’s morning session

## Slide 6
II. Neutrino Cross-Section
  Same nuclear target and transferable to FD
  Challenge:
    Varying flux alters neutrino interactions, as cross-section depends on neutrino energy
    Differences in ND efficiency and acceptance shift the kinematic phase space of interactions detected at each site
III. Detector Uncertainties
  Similar detector technologies
  Challenge: different fluxes, high pile-up at ND
Formaggio and Zeller
Rev. Mod. Phys. 84, 1307
requirements for a near detector?
Zoya Vallari, NNN 2024
Image Credit: Luke Pickering

## Slide 7: LArTPC: A short primer
Zoya Vallari, NNN 2024

## Slide 8: What is^ LArTPC?
Neutrino interaction in LAr produces ionization and scintillation light
The ionization charge drifts in a uniform electric field to finely segmented wire planes.
Multiple wire orientations give independent views of the same event.
Image credit: WirecellTeam, BNL
a Classical

## Slide 9: Why LArTPCs?
Exquisite imaging for flavor ID and energy reconstruction.
Excellent particle identification and spatial resolution.
Low thresholds for charged particles enables precise reconstruction of lepton and hadronic energy.
ne + Ar → e p p p-
nm + Ar → m p p p0

## Slide 10: LArtPC Program at Fermilab
Image Credit: Marco Del Tutto

## Slide 11: near detector for short-baseline
Zoya Vallari, NNN 2024
Image Credit: Marco Del Tutto

## Slide 12: highlights of sbnd design
Two TPCs that share a central HV cathode (CPA)
Four anodes (APA) with 3 wire planes each
  1 collection (vertical), 2 induction (±60°)
  3 mm spacing both inter-wire and inter-planes
Photon Detection System (PDS)
  120 8'' PMTs
  192 X-ARAPUCAs (developed in Brazil)
  Reflective foil panels coated with wavelength shifter embedded into the CPA
  Light-yield ≥100 pe/MeV
Cosmic Ray Tagger (CRT)
More details in the talk
by Gustavo Valdiviesso yesterday!
Zoya Vallari, NNN 2024
Summarized from slides by Gustavo Valdiviesso

## Slide 13: SBND is taking beautiful data, and we are looking forward to seeing first results!
Zoya Vallari, NNN 2024

## Slide 14: near detector for long-baseline
Zoya Vallari, NNN 2024

## Slide 15: next generation LArTPCs But Why?
Pixel readout
Anode plane
Zoya Vallari, NNN 2024

## Slide 16: LBNF Pip-II Beam: most powerful accelerator neutrino beam in the world
Neutrino-mode beam at ND
Plot Credit: Luke Pickering
Zoya Vallari, NNN 2024

## Slide 17: ND LArTPC in the DUNE beam
Single neutrino interaction
~50 n interactions in a single 1.2 MW LBNF beam spill

## Slide 18: LArTPCs in high-pile up environment
Conventional TPCs infer 3D reconstruction by combining 2D views.
Ambiguities in projective wire readout aggravate in high multiplicity environment
Classical
X. Qian et al 2018 JINST 13 P05032
True simulated
event
Processed signal and
sophisticated reconstruction
algorithms
Raw time &
geometry based
reconstruction

## Slide 19: how to maintain signal fidelity in a high occupancy environment?
Zoya Vallari, NNN 2024

## Slide 20: A next generation of lartpc
Pixelated Charge readout
Modular TPC
Optical Segmentation
Low-profile field cage
Zoya Vallari, NNN 2024

## Slide 21: pixelated charge readout
Integrating amplifier with self-triggered digitization and readout
  Integrates charge for ~3s (4 mm drift), then digitizes
Always active – continuous self-triggering
Achieve low power by avoiding digitization and readout of mostly quiescent data
Charge-sensitive amplifier
Self-triggering discriminator
Standard SAR Digitizer
Not covered*: Q-Pix technology by Dave Nygren (UTA) and Yuan Mei (LBNL) arXiv: 1809.10213
Dan Dwyer et al. JINST 13 (2018) P10007

## Slide 22: pixel tiles
32 cm x 32 cm large-format mixed signal PCB
Front : 4900-pixel pads with 4.4 mm pixel pitch
Back: 10x10 grid of LArPix ASICs
Mass production by commercial vendors
  ~0.10 USD/channel
LArPix-v2a ASIC
Notes: PCB: Printed Circuit Board

## Slide 23: dynamic hydra i/o configuration
Serial I/O data rate is slow (~5 Mb/s per I/O channel) to limit digital power
Hydra I/O: novel adaptable chip-to-chip communication to avoid single point failures
Notes: In Hydra-I/O, the system’s networks can be automatically reconfigured to route around individual failed ASICs without compromising the overall network, which ensures system reliability in extreme environments like the ND.
Modest data volumes: ~1 MB/s per square meter of anode in surface cosmic-ray flux
Hydra I/O is a system to create ad-hoc, software-defined networks of Application-Specific Integrated Circuits (ASICs) that can be automatically reconfigured to route around individual failed ASICs without compromising the overall network.

## Slide 24: native 3D imaging
Unambiguous tracking of charged particles
True 3D imaging of TPC ionization
Zoya Vallari, NNN 2024

## Slide 25: Short interlude: Next gen detectors require next gen software
Zoya Vallari, NNN 2024

## Slide 26: pixelated Design is well-suited for GPU processing
  Advanced simulation leveraging highly parallelized processing.
    Consistent processing time even as the number of pixels increased.
    Benchmarked against cosmic data, demonstrating its high maturity.
  Machine-learning based reconstruction integrate seamlessly to GPU computing.
A. Abed Abud et al 2023 JINST 18 P04034
Highly-parallelized simulation of a pixelated LArTPC on a GPU

## Slide 27: modular TPC with optical segmentation
  To simplify charge-light signal matching combinatorics, modularize the TPCs and add optical segmentation.
    Creates short drift distances (~50 cm) with contained scintillation light
Single neutrino interaction

## Slide 28: modular TPC with optical segmentation
Single neutrino interaction
Light flashes in a single TPC
Charge deposit in a single TPC
  To simplify charge-light signal matching combinatorics, modularize the TPCs and add optical segmentation.
    Creates short drift distances (~50 cm) with contained scintillation light

## Slide 29: Light readout system
Thin-profile VUV sensitive light-traps perpendicular to the pixelated anode.
96 SiPMs per TPC provide 25% photo-coverage.
Two complementary light traps with shared readout electronics:
  ArCLight (ArgonCube light detector)
    30 cm x 50 cm x 1 cm
    6 SiPM channels
  LCM (light collection module)
    10 cm x 50 cm x 1 cm
    2 SiPM channels
Zoya Vallari, NNN 2024
Notes: How are these different from XARAPUCA light traps?

## Slide 30: Light readout system
 | ArCLight | LCM
Photon Detection Efficiency | ~0.2% | ~0.6%
Spatial resolution | ~5cm | ~10cm
Strengths | High dynamic range | ~2 ns time resolution @200 PE
Zoya Vallari, NNN 2024
Notes: How are these different from XARAPUCA light traps? The LCM shows an average efficiency of 0.6%, which enables a light trigger for events depositing MeV-scale energies, with an accurate scintillation amplitude and energy reconstruction.

## Slide 31: Putting it all together: A Modular LArTPC
Zoya Vallari, NNN 2024

## Slide 32: Technical Demos
x 4
2x2 Cryostat
Single LAr Cube
2018–2020
Demonstration of individual novel technologies
2020
Single cube prototypes: First combined test of charge readout and light readout systems
2021–2023
Single module demonstrators: Ton-scale, fully-integrated prototype of ND-LAr module measuring cosmic rays.
2024
2x2 demonstrator: Designed with four single modules in the neutrino beam at Fermilab.

## Slide 33: Single Module Demonstrators
Collected O(100)M cosmic ray events with successful operation of four ton-scale LArTPC modules
Notes: four fully-integrated ton-scale O(100k) pixel channel systems
Collected >100 M cosmic-ray events

## Slide 34: Single module operations
Operations met all requirements for DUNE ND-LAr design:
  Stable HV at ~30kV (~1 kV/cm drift, 2x target)
  Stable Purity at >2ms (>4x target)
  MIP Charge Signal-to-Noise >20:1 (at target)
  No component failures during operation
With high statistics data, modular LArTPC program is already producing competitive measurements.
A. Abed Abud et al Instruments 2024, 8(3), 41
Performance of a modular Ton-scale
Pixel-Readout Liquid Argon
Time Projection Chamber
Notes: ~950 e ENC(ENC: equivalent noise charge)

## Slide 35: charge-light matching
Michel electrons from the stopping muon are an important standard candle.
~2 μs muon lifetime is shorter than the drift speed leading to negligible position displacement but a clear signature in the timing signal given the ns-scale resolution.
Zoya Vallari, NNN 2024
A. Abed Abud et al Instruments 2024, 8(3), 41
Notes: a long muon track ending with a Bragg peak followed by a short ionization track from the electron at a different angle with respect to the muon direction.

## Slide 36: 2x2 Demonstrator
LArTPC Modules
First DUNE (prototype) detector
to take neutrino beam data!
4 LArTPC modules assembled as a prototype detector with repurposed scintillator planes from Minerva providing tracking.

## Slide 37: 2x2 Demonstrator
First DUNE (prototype) detector
to take neutrino beam data!
Plot Credit: Callum Wilkinson
4 LArTPC modules assembled as a prototype detector with repurposed scintillator planes from Minerva providing tracking.
A run in the NuMI beam provides comparable intensity to the LBNF beam.

## Slide 38: 2x2 Demonstrator
4 LArTPC modules assembled as a prototype detector with repurposed scintillator planes from Minerva providing tracking.
A run in the NuMI beam provides comparable intensity to the LBNF beam.
2x2 collected few days of high purity neutrino beam data in July 2024.
First DUNE (prototype) detector
to take neutrino beam data!

## Slide 39
Zoya Vallari, NNN 2024

## Slide 40: summary
Zoya Vallari, NNN 2024

## Slide 41: DUNE ND-LAr next generation TPC
5 x 7 array of LAr TPC modules (1 m x 1m x 3m) with ~67t Fiducial Volume
To cope with the extremely high-multiplicity environment of the most powerful accelerator neutrino beam, DUNE ND-LAr employs multiple advanced technologies for next-generation LArTPCs:
  ~14M pixels across a 5 x 7 array of TPC modules
  Central cathode
  Two anode planes of PCB tiles with gold-plated pixel pads and LArPix ASICs on opposite sides
  Optically segmented modular design with 50 cm drift
  Resistive shell field cage with light detection modules on the side

## Slide 42
Image by R. Soleti
We are excited to embrace the challenge of “too-many-neutrinos” in the precision era of neutrino physics.
We aim to capture every neutrino interaction—pixel by pixel!!
Zoya Vallari, NNN 2024

## Slide 43: SUPPLEMENTARY SLIDES
Zoya Vallari, NNN 2024

## Slide 44: DUNE ND Complex
To achieve its ambitious physics goals, DUNE will need to constrain its systematics to a few percent level.
A suite of near detectors are designed to robustly constrain systematics and achieve required sensitivities.
Muon-range
spectrometer
System for On-Axis Neutrino Detection
Downstream Magnetized Tracker
(such as TMS)
PRISM
System for moving the LArTPC and tracker up to 30m transverse to the beam
Beam
axis

## Slide 45: Dune nd requirements
ND-LAr
TMS
SAND
Measurements transferable to the FD
Constrain the cross-section model
Measure the neutrino flux
Obtain measurement with different fluxes
Monitor time variations of the neutrino beam
Operate in high-rate environment
New exciting physics measurements to test BSM, sterile and dark-matter models.

## Slide 46: LArPix specifications
Specification | Value | Comment
Analog inputs | 64 | Single-ended input
Gain | 4.5 V/e- | 
Power | <200 W/channel | Static power dissipation
Dynamic range | 1.3 V | Chip configurable
ADC resolution | 8 bits | 
ADC LSB | 4 mV | Chip configurable
Threshold range | 0 to 1.8 V | Channel configurable
Threshold resolution | 1.5 mV | 
Channel linearity | < 1.2% | Pre-calibration
Multi-hit separation time | 1.2 s | Chip configurable
Operating temperature | 80 to 300 K | 
Specification | Value | Comment
Analog inputs | 64 | Single-ended input
Gain |  | 
Power |  | Static power dissipation
Dynamic range | 1.3 V | Chip configurable
ADC resolution | 8 bits | 
ADC LSB | 4 mV | Chip configurable
Threshold range | 0 to 1.8 V | Channel configurable
Threshold resolution | 1.5 mV | 
Channel linearity | < 1.2% | Pre-calibration
Multi-hit separation time |  | Chip configurable
Operating temperature | 80 to 300 K | 
Specification | Value | Comment
Heat density | ~13 mW/ASIC | 
Pixel multiplexing | 6.4k channels/cable | 
Noise | ~850 e- ENC | 
Tile leakage current | < 5 e- / 500 s | 
Charge resolution | < 1200 e- | < 5% MIP charge
Spatial resolution | 1.1 to 1.3 mm | Geometry dependent
Timing resolution | 0.7 s | Chip configurable
Saturation level | > 200 ke- | 
Triggering efficiency | ~80% for MIP | 
MIP S:N | >20:1 | 
Specification | Value | Comment
Heat density | ~13 mW/ASIC | 
Pixel multiplexing | 6.4k channels/cable | 
Noise | ~850 e- ENC | 
Tile leakage current |  | 
Charge resolution | < 1200 e- | < 5% MIP charge
Spatial resolution | 1.1 to 1.3 mm | Geometry dependent
Timing resolution |  | Chip configurable
Saturation level | > 200 ke- | 
Triggering efficiency | ~80% for MIP | 
MIP S:N | >20:1 | 

## Slide 47
2x2 MINOS Hall Underground Installation @Fermilab